## Slide 1: Lake Thunderbird Water Quality Trends
June 3, 2022

## Slide 2: Exploratory Data Analysis
Affects Study Design
Is the data suitable for trends analysis
  Adequate data
  Both period of record and timestep
Period of Record
  Hydrologic Variation
  Climatological Variation
  Physical Variation
Timestep
  Data intermittency issues (short term interruptions)
  Inadequate seasonality
  Data gaps (long-term interruptions)
Parameter Selection

## Slide 3
Parameter Selection
Watershed characteristics
Stressor variables
  Eutrophication
  Sedimentation
Response variables
  Water Clarity
  Transparency (i.e., Available Light)
  Biologic Response (algal chlorophyll and pheophytin, plankton community dynamics)
Nutrients (N and P) enter the lake through external loading from the surrounding watershed and internal recycling processes
Nutrients and light stimulate the growth of phytoplankton and macrophytes (aquatic plants)
Aquatic plants consume carbon dioxide and the increase the pH of the lake
Zooplankton (aquatic invertebrates) graze on the phytoplankton population
Aquatic plants break down and or die, consume oxygen as part of decomposition, and recycle ammonia, phosphorus, and carbon dioxide into the water and the sediments

## Slide 4: Parameter Selection
Analyzed Surface Parameters | Unit | Indicator Type
Turbidity | NTU | Sedimentation stressor and response
Secchi Disk Depth | cm | Eutrophication stressor and response
Total Alkalinity | mg/L | Watershed geology
Total Hardness | mg/L | Watershed geology
Chlorophyll a | µg/L | Eutrophication stressor response
Pheophytin-a | µg/L | Eutrophication stressor response
Ammonia as N | mg/L | Eutrophication stressor
Inorganic Nitrogen as N | mg/L | Eutrophication stressor
Total Nitrogen as N | mg/L | Eutrophication stressor
Total Phosphorous as P | mg/L | Eutrophication stressor

## Slide 5: Exploratory Data Analysis
Spatial Analysis
  Is the lake adequately represented both ecologically and hydrologically?
  Can stations be aggregated?
Data Analysis
  What is the condition of the data
  Look at both distribution and shape
  Affects statistical analysis and interpretation

## Slide 6: Reservoir Ecological Zones

## Slide 7
Monitoring ID | Name | Ecological Zone Assignment
520810000020-01 | Sta 1 | Lacustrine
520810000020-02 | Sta 2 | Lacustrine
520810000020-04 | Sta 4 | Lacustrine
520810000020-12 | Sta 12 | Lacustrine
520810000020-03 | Sta 3 | Hog Creek Transition
520810000020-08 | Sta 8 | Hog Creek Riverine
520810000020-05 | Sta 5 | Little River Transition
520810000020-07 | Sta 7 | Little River Transition
520810000020-06 | Sta 6 | Little River Riverine?
520810000020-11 | Sta 11 | Dave Blue Creek Riverine

## Slide 8
Station | Ecological Zone Assignment
Stations 1, 2, 4 | Lacustrine
Station 3 | Hog Creek Transition
Station 8 | Hog Creek Riverine
Stations 5, 7 | Little River Transition
Station 6 | Little River Riverine
Station 11 | Dave Blue Creek Riverine

## Slide 9: Data Analysis – Distribution and Shape

## Slide 10: Data Analysis – Trends
Regression
  Most commonly used in controlled designs
  Assumes normal distribution, data independence, equal variance
Seasonal Kendall
  Utility and bias not reliant on assumptions
  Adjusts data for and test results for user-defined seasonal effects
Confidence Level and Trend Likelihood
Confidence Level | Trend Likelihood
<80% | Unlikely
80% to <90% | Indeterminant
90% to <95% | Likely
95% to <99% | Very Likely
99% and greater | Highly Likely

## Slide 11: Trend Summary—Nutrients
Nutrients
Know that both TP and TN are high in the reservoir
Generally both showed no significant trend
For TN, showed a likely increasing trend in lacustrine
For TP, showed a likely decreasing trend in Little River Transition

## Slide 12: Trend Summary—Clarity and Transparency
Ecological Zone |  | 2000 | 2020 | Trend Likelihood for Turbidity | slope (NTU/L*yr -1)
Lacustrine |  | 8.9 | 8.3 | Unlikely | -0.02
Transition | Little River | 14.9 | 14.9 | Unlikely | 0.00
 | Hog Creek | 12.7 | 11.0 | Indeterminant | -0.07
Riverine | Little River | 44.6 | 53.7 | Indeterminant | 0.45
Riverine | Hog Creek | 32.5 | 20 | Highly Likely to decrease | -1.00
Dave Blue Creek |  | 45 | 32.5 | Likely to decrease | -1.11
Ecological Zone |  | 2000 | 2020 | Trend Likelihood for Secchi Disc | slope (cm/L*yr-1)
Lacustrine |  | 76.7 | 64.2 | Highly Likely | -0.63
Transition | Little River | 54.9 | 43.7 | Highly | -0.35
 | Hog Creek | 59.1 | 50.2 | Highly | -0.45
Riverine | Little River | 21.4 | 16.3 | Highly | -0.35
Riverine | Hog Creek | 29.9 | 31.8 | Unlikely | 0.12
Dave Blue Creek |  | 24.9 | 23.4 | Unlikely | -0.12

## Slide 13: Trend Summary—Chlorophyll and Pheophytin
Ecological Zone |  | 2000 | 2020 | Trend Likelihood for Chlorophyll | slope (µg/L*yr-1)
Lacustrine |  | 11.6 | 20.8 | Highly | 0.45
Transition | Little River | 12.8 | 25.7 | Highly | 0.64
 | Hog Creek | 12.0 | 24.3 | Highly | 0.60
Riverine | Little River | 19.0 | 32.7 | Highly | 0.67
Riverine | Hog Creek | 28.3 | 21.3 | Very | -0.5
Dave Blue Creek |  | 39 | 26.3 | Highly | -1.12
Ecological Zone |  | Trend Likelihood for Pheophytin
Lacustrine |  | Highly
Transition | Little River | Highly
 | Hog Creek | Highly
Riverine | Little River | Highly
Riverine | Hog Creek | Very
Dave Blue Creek |  | Highly

## Slide 14: Reservoir Ecological Model
Following a longitudinal gradient
Nutrient Stressors
  higher in riverine to lower in lacustrine
  Source in upper end is watershed
  Source in lower end is internal cycling
Turbidity
  Upper end has high TSS upper end and is Light-limited
  Lower end is clear with no light limiting
Response
  Upper end mostly tending eutrophic
  Become more oligotrophic toward lower end
  High transparency

## Slide 15: Thunderbird Attributes
Nutrients are at excessive levels throughout the reservoir
  Are showing some decrease in the Little River transition zone
  Need to understand nutrient entrainment and recycling better
Turbidity generally becomes lower as move through the lake
  This is generally in line with the attribute model
  Turbidity impairment mostly result of suspended solids in riverine zones of lake
  Decreasing inorganic solids (turbidity) in the Hog Creek and Dave Blue Creek riverine zones suggest significant land use changes
Cultural eutrophication continues to be an ongoing and worsening process throughout the reservoir
  Chlorophyll-a is increasing significantly in lacustrine, transition and Little River
  As a corollary, transparency is significantly decreasing
  Additionally, increasing pheophytin is indicative of continual algal die-offs
  Conversely, have a significant decrease in chlorophyll-a in Hog and Dave Blue Creek but still considered hyper-eutrophic
  Transparency shows a leveling in these areas, as well

## Slide 16: Recommendations
External vs Internal nutrient sources
Determine links between land use features and external load
Long-term trend analysis requires consistency
  Prioritize Stations, parameters, sample frequency
  Laboratory methods (detection limits)

## Slide 17: QUESTIONS?

## Slide 18
Thank You
SDOX